## Slide 1: Digital Logic Design and Lab
Term Project : Number Baseball Accelerator(NBA) Design

## Slide 2: Contents
What is Number Baseball
Goal
Restriction on implementation
Default algorithm
Submission list

## Slide 3: Contents
What is Number Baseball
Goal
Restriction on implementation
Default algorithm
Submission list

## Slide 4: Number Baseball
Number Baseball is a number game
One player (grader) makes random 4-digit decimal number (0123~9876) with different number for each digit.
The other player (solver) guesses the number
Whenever solver gives the answer, grader responds with ‘ball’ or ‘strike’ according to the following rules
Ball : Right number, but wrong location
Strike : Right number and location
EX) Correct answer : 1234 , Try : 1829 => 1strike,1ball
It continues until solver gives the right answer(4 strike) to grader

## Slide 5: Contents
What is Number Baseball
Goal
Restriction on implementation
Default algorithm
Submission list

## Slide 6: Goal
Design a Number Baseball accelerator
  Goal : implement solver in Verilog code
  Find out the best way for solver to give the correct answer with the least number of attempts as possible

## Slide 7: Contents
What is Number Baseball
Goal
Restriction on implementation
Default algorithm
Submission list

## Slide 8: Restriction on implementation
There are two main top modules
: ‘solver’ , ‘grader’
solver :
  Decide number to ask and transfer the number to ‘grader’ module
  Receive ‘ball’ or ‘strike’ from ‘grader’ module
  Implemented with FSM
grader
  Determine whether the number transferred from ‘solver’ module is ‘ball’ or ‘strike’
  Send back ‘strike’ or ‘ball’ to ‘solver’ module

## Slide 9: Restriction on implementation
The zip file including skeleton of solver module, grader, testbench and other necessary files will be given in the code uploaded to ETL
  tb_nba.v, grader.v and solver.v are in rtl folder
Your code will be graded by original grader and testbench uploaded in ETL. (answer list will be different)
  Never change the interface of solver and grader
  Never change the Verilog code of grader
  Never change the Verilog code of testbench
  If you change the code, you may not be correctly graded

## Slide 10: Restriction on implementation
Communication protocol between solver and grader
  The solver's question is determined to be delivered to the grader when the solver's valid and the grader's ready are 1 at the positive edge. (handshake occurs)
    The channel through which the solver's questions are delivered is defined as a question channel
  The grader’s strike and ball are determined to be delivered to the solver when the grader’s valid and the solver's ready are 1 at the positive edge. (handshake occurs)
    The channel through which the strike and ball are transmitted is defined as the sb channel
  the VALID signal of the solver must not be dependent on the READY signal of the estimator receiving that information
  solver can wait until it detects a VALID signal before it asserts its corresponding READY signal.
  While it is acceptable to wait for VALID of estimator to be asserted before asserting READY of solver , it is also acceptable to assert READY of solver before detecting the corresponding VALID of estimator. This can result in a more efficient design.

## Slide 11: Restriction on implementation
Description of grader
  Please refer to grader Verilog code uploaded in ETL
  Behavior related to grader valid signal
    When a handshake occurs in the question channel, the grader calculates the strike and ball and drives the calculated strike and ball to the output port while changing the grader valid signal to 1.
    When the grader valid signal is 0, invalid strike and ball signals are driven to the output port even after the question channel handshake has occurred.
    When the sb channel handshake occurs, the grader valid value remains 0 until the next question channel handshake occurs.
  Behavior related to grader ready signal
    The grader maintains grader ready as 0 after the question channel handshake has occurred until the sb channel handshake has occurred.
    The grader changes grader ready to 0 when solver valid is 0 in the clock's posedge.
  Behavior related to counting
    The grader increments the count by one each time a question channel handshake occurs.
    If the solver can not solve the problem by the time the count reaches 200, testbench will force to move on to the next round with reset signal asserted.
    If the question channel handshake or sb channel handshake does not occur during 200 cycles, it is determined that deadlock has occurred, and the count is increased to 200, and the next round will be started with the reset signal asserted.

## Slide 12: Restriction on implementation
Description of testbench
  Please refer to the code of testbench
  Testbench reads the answers.txt and give the answer of the current round to the grader.
  Testbench will run 1024 rounds.
  When the count of the grader reaches 200 or Correct signal changes to 1, the current round will end and the next round will start.
Restriction of solver
  If the behavior of the grader is not properly considered, incorrect operation or deadlock may occur.
  You must use synchronous active low reset.

## Slide 13: Restriction on implementation
Reference waveform
Question channel handshake :
sb channel handshake :

## Slide 14: Restriction on implementation
Setting to run the given testbench
  Unzip given term_project .zip
  You should create the modelsim project in <path to term_project>/term_project/projects/
    Never use Korean in the path
  Please be careful not to mix up term project codes with your previous codes in work library

## Slide 15: Contents
What is Number Baseball
Goal
Restriction on implementation
Default algorithm
Submission list

## Slide 16: Algorithm Example
You can use the below algorithms for implementation of ‘solver’ module
This is a simple algorithms, and you can improve algorithm or use the different algorithm. But, you should get less than 30 counts in average.
But you can’t use the same 4-digit numbers as answer or question. EX) 0000
Simple Algorithm (Example is answer 6247)
  1. Start the first question with 0123.
    Grader returns 0 strike 1 ball.
    Strike + ball = 1 is reference sum
    If grader returns strike + ball = 4 (reference sum) at any time, move on to step 6.

## Slide 17: Algorithm Example
  2. Change the first position number and find the change of reference sum (Ex. answer = 6247)
    Reference sum (strike + ball) is 1
    Reference question is 0123
    Try to ask question 4123, 5123, 6123, etc.
    If grader returns strike + ball = 4 (reference sum) at any time, move on to step 6.
    In this example, question 4123 is 0 strike 2 ball, and strike + ball = 2.
    If strike + ball(=2) > reference sum(=1), 4 is the valid number.
    Save the valid number and fix the first position to number 4.
    Now, reference sum is the strike + ball =2

## Slide 18: Algorithm Example
  3. Change the second position number and find the change of reference sum (Ex. answer = 6247)
    Reference sum (strike + ball) is 2
    Reference question is 4123
    Try to ask question 4023, 4523, 4623, etc.
    If grader returns strike + ball = 4 (reference sum) at any time, move on to step 6.
    In this example, question 4023 is 0 strike 2 ball, and strike + ball = 2. No change reference sum.
    question 4523 is 0 strike 2 ball, and strike + ball = 2. No change reference sum.
    question 4623 is 0 strike 3 ball, and strike + ball = 3. Reference sum changes.
    If strike + ball(=3) > reference sum(=2), 6 is the valid number.
    Save the valid number and fix the second position to number 6.
    Now, reference sum is the strike + ball =3

## Slide 19: Algorithm Example
  4. Change the third position number and find the change of reference sum (Ex. answer = 6247)
    Reference sum (strike + ball) is 3
    Reference question is 4623
    Try to ask question 4603, 4613, 4653, etc.
    If grader returns strike + ball = 4 (reference sum) at any time, move on to step 6.
    In this example, question 4603 is 0 strike 2 ball, and strike + ball = 2. Reference sum changes.
    If strike + ball(=2) < reference sum(=3), the third position of reference question 4623, number 2 is the valid number.
    Save the valid number and fix the third position to number 2.
    Now, reference sum is the strike + ball = 3

## Slide 20: Algorithm Example
  5. Change the fourth position number and find the change of reference sum (Ex. answer = 6247)
    Reference sum (strike + ball) is 3
    Reference question is 4623
    Try to ask question 4620, 4621, 4623, 4624, 4625, 4627, etc. until you find the strike + ball = 4
    In this example, question 4627 is 1 strike 3 ball, and strike + ball = 4.
    Save the valid number and fix the fourth position to number 7.
    You found all the valid numbers.

## Slide 21: Algorithm Example
  6. Change the fourth position number and find the change of reference sum (Ex. answer = 6247)
    Reference question is 4627 and this is all valid numbers.
    Try to ask question 4627, 4672, 4726, 4762, 4267, 4276, 6274, 6427, 6247, etc.
    The number of all cases is 24.
    If grader returns 4 strike 0 ball, This is correct.
    Example count:
      0123, 4123, 4023, 4523, 4623, 4603, 4620, 4621, 4623, 4624, 4625, 4627, 4672, 4726, 4762, 4267, 4276, 6247(correct)
      Count is 18.

## Slide 22: Contents
What is Number Baseball
Goal
Restriction on implementation
Default algorithm
Submission list

## Slide 23: Submission list
Due date : 12/15 (Thursday) 23:59. submit your code in ETL.
Report
  Explain your solver code
  Analyze simulation results of your code
Source code
  Verilog code for solver
  File name : <student_id>_solver.v
    EX) 2022_12345_solver.v
  Don’t submit .zip file
  If you don’t follow this format, you may not be correctly graded.

## Slide 24: Grade
Submitted codes will be graded according to the average number of count taken to give correct answer for all rounds
Percentage
  Code : 80%
  Report : 20%
Extra point for improving the algorithm